## Slide 1: Microcontroller Project
Electronic Engineering
Wiktor, Vytaras, HermaNn, Alexander, Pina

## Slide 2: Contents
Building
Arduino
  Line Tracking
  Ultrasonic Sensors
RaspberryPi
  Berkeley Socket
  Camera
QT

## Slide 3: Building – Wooden ELE-Bot Kit
Wooden Panels + Bolts
LiPO (11.1V , 3200mAh)
DC-Motor
Arduino UNO + Motorshield
Line Tracking Sensor
Ultrasonic Sensor
RaspberryPi + L298 Motor Board
Raspberry Pi Camera v.2
USB-Powerblock (5V, 5200 mAh)

## Slide 4
Testing phase

## Slide 5: Arduino Setup + InfraRed

## Slide 6: Infrared
2 Infrared Sensors
Black Line is in between
If one sensor gets on the line it turns in this direction

## Slide 7: Ultrasonic + Avoidance

## Slide 8: Ultrasonic
3 Ultrasonic Sensors
30cm to detect obstacle
While avoiding: If it senses obstacles within < 50cm it turns away
Car drives a curve around it
Car can avoid on either left or right side
When it detects Black line while avoiding it starts following again

## Slide 9: Berkeley Socket
TCP Socket API
  General Setup for Server and Client
  Common interface for input and output to streams of data
  Since 1983
Official Code examples on Wikipedia to include in your projects

## Slide 10: RaspiCam Stream
Client side
Reduce resolution to 200x200
  Put into byte stream
  Convert bytes to characters
  Send the characters
Server side
Receive characters
Convert characters to byte stream
Map the characters to Matrix
RGB values
Construct Image 640x480

## Slide 11: QT